Lesson Plan

Name of faculty:	ASHOK KUMAR, AP-ECE

Discipline:	ECE

Semester:	4TH

Subject:	ANALOG ELECTRONICS

Lesson Plan Duration: 15 weeks (from January, 2018 to April, 2018)

Work Load(Lecture/Practical) per week (in hours): Lectures:  03 hours, Tutorials:02hours

| Week | Theory | Practical |
| --- | --- | --- |
|  | Lecture day | Topic(Including assignment/ test) | Practical day | Topic |
| 1st |  | Voltage amplifier, current amplifier | 1 | To design a simple Common emitter (CE) amplifier circuit using BJT & find its gain & frequency response. |
|  |  | Trans-conductance amplifier& trans-resistance amplifier |  |  |
|  |  | Biasing scheme for BJT |  |  |
| 2nd |  | Biasing scheme for FET | 2 | To design a differential amplifier using BJT & find its gain & frequency response |
|  |  | Bias- stability , various configuration such CE/CS |  |  |
|  |  | CB/CG , CC/CD & their features |  |  |
| 3rd |  | Small signal analysis | 3 | To design RC coupled Single stage BJT amplifier & determination of gain , frequency response, input & output impedences.. |
|  |  | Low frequency transistor model |  |  |
|  |  | Estimation of voltage gain, input resistance, output resistance |  |  |
| 4th |  | Design procedure for particular specification | 4 | To design a BJT Emitter follower & determination of gain , frequency response, input & output impedences.. |
|  |  | Low frequency analysis of multistage amplifier |  |  |
|  |  | High frequency transistor model |  |  |
| 5th |  | Frequency response of single stage amplifier | 5 | To design & test the performance of BJT-RC phase oscillator for fo <= 10 khz |
|  |  | Multistage amplifier |  |  |
|  |  | cascade amplifier |  |  |
| 6th |  | Various classes of operation Class-A | 6 | To design & test the performance of BJT-Hartley oscillator for fo >= 100 khz |
|  |  | Class-B |  |  |
|  |  | Class-AB |  |  |
| 7th |  | Class-C | 7 | To design & test the performance of BJT-Colpitts oscillator for fo >= 100 khz |
|  |  | Power efficiency & linearity issues |  |  |
|  |  | Voltage series feedback |  |  |
| 8th |  | Current series feedback | 8 | To design Astable multivibrator using 555 timer. |
|  |  | Voltage shunt , Current shunt |  |  |
|  |  | Effect of feedback on gain , bandwidth etc. |  |  |
| 9th |  | Calculation with practical circuit | 9 | To design Monostable multivibrator using 555 timer. |
|  |  | Concept of stability |  |  |
|  |  | Gain margin & phase margin |  |  |
| 10th |  | Review of basics concept : Barkhausen criterion for oscillator | 10 | To design Schmitt trigget using op-amp &verify its operational characterstics. |
|  |  | RC phase shift oscillator |  |  |
|  |  | Wein bridge oscillator |  |  |
| 11th |  | Hartlay oscillator | 11 | Revision |
|  |  | Collipts oscillator , Clapp oscillator |  |  |
|  |  | 555 Timer as Monostable & Astable multivibrator |  |  |
| 12th |  | Schmitt trigger & its application | 12 | Revision |
|  |  | Current mirror: basic topology& its variants |  |  |
|  |  | Output resistance & minimum sustainable volatge |  |  |
| 13th |  | Minimum usable load | 13 | Revision |
|  |  | Differential amplifier |  |  |
|  |  | Basic structure & principle of operation |  |  |
| 14th |  | Calculation of differential gain | 14 | Revision |
|  |  | Common mode gain |  |  |
|  |  | CMRR & ICMR |  |  |
| 15th |  | Op -amp design | 15 | Viva- Voice |
|  |  | Design of differential amplifier for a given specification |  |  |
|  |  | Design for gain stages & output stages |  |  |